-----------------------------------------------------------------

The following is a news release from Master Bond Inc. You have received it because you are listed as an editor for your publication.

Attached to this email is a low resolution version of the photograph that is included in the press kit for this product.

High resolution version of this image and files with the body text of this release in Word, HTML and text formats are available at http://www.masterbond.com/newsrelease/mastersil156.

-----------------------------------------------------------------

## FOR IMMEDIATE RELEASE

## Thermally Conductive Two Component Silicone Meets UL 94V-0 Specification for Flame Retardancy

## In addition to typical silicone properties such as flexibility and high temperature resistance, Master Bond MasterSil 156 passes the rigorous UL 94V-0 tests for flame retardancy. This two part silicone system is addition cured and does not require exposure to air for complete cross-linking. It has a convenient one to one mix ratio by weight and will not outgas while curing.

## Formulated for potting, encapsulation and sealing applications, MasterSil 156 is a competent electrical insulator with a low viscosity that can cure in sections beyond 1-2 inches thick. It is thermally conductive and is temperature rated to 105°C by UL in thicknesses up to ¼ inch and above. Its flexibility allows it to withstand aggressive thermal cycling and resist vibration and shock. Also, it is very resistant to water, humidity, oils and other environmental elements.

## MasterSil 156 bonds well to a wide variety of substrates including metals, composites, glass, ceramics and many rubbers and plastics. Since it is 100% solids and contains no solvents, its shrinkage upon cure is very low. It is available in a variety of standard packaging options ranging from ½ pint to 5 gallon container kits. This silicone has a 6 month shelf life at room temperature when stored in original, unopened containers.

## Master Bond Potting and Encapsulation Compounds

Thermally conductive, flame retardant MasterSil 156 has good flow and electrical insulation properties, enabling it to be well suited for potting, sealing and encapsulation applications. Read more about Master Bond’s potting and encapsulation compounds at http://www.masterbond.com/applications/potting-and-encapsulation or contact Tech Support. Phone: +1-201-343-8983 Fax: +1-201-343-2132 Email: technical@masterbond.com.

Note to Editors:

For a full product description, please visit: http://www.masterbond.com/tds/mastersil-156

Our video on MasterSil 156 is available here: http://youtu.be/5N0UYaKk2s4

Check out product videos on our YouTube channel: http://www.youtube.com/user/MasterBondVideo

You can embed any of our videos on your website.

CONTACT

James Brenner, Marketing Manager

Email: jbrenner@masterbond.com

Tel: +1-201-343-8983

Fax: +1-201-343-2132

MASTER BOND INC

154 Hobart Street

Hackensack, NJ 07601-3922

Web: www.masterbond.com

# # #